## Slide 1
How Fast Is Your Kernel, Really?
Profiling SOTA GPU Kernels with torch.profiler and Nsight Compute
Aheli Poddar
Associate Software Engineer, Red Hat PyTorch
IISC Bangalore
NVIDIA H200 • SM 9.0 • 143 GB HBM3e
1/36

## Slide 2
What We’ll Cover
DeepGEMM FP8
3.09x over bf16 cuBLAS
JIT-compiled FP8 GEMM from DeepSeek
FlashAttention-3
2.0–2.6x over FA-2
Hopper-native attention with WGMMA + TMA
SonicMoE
35 TFLOPS on H200
IO-aware MoE kernels from Tri Dao
Each kernel: Code → Perfetto Trace → NCU Deep Dive
2/36

## Slide 3
The Profiling Stack
torch.profiler
Perfetto UI
Temporal view: WHEN kernels run
Nsight Compute (ncu)
NCU GUI
Hardware view: HOW kernels use the GPU
torch.profiler tells you WHAT happened. NCU tells you WHY.
3/36

## Slide 4
KERNEL 1
DeepGEMM: JIT-Compiled FP8 GEMM
github.com/deepseek-ai/DeepGEMM
3.09x faster than bf16 cuBLAS on H200
4/36

## Slide 5
What is FP8?
E4M3 Format: [S] [E E E E] [M M M]
3 mantissa bits — optimized for forward pass / inference
Block-scaled quantization: every 128 elements gets an FP32 scale factor
Replaces the per-tensor scaling of classic INT8 quantization
2x Tensor Core throughput, half the data size
5/36

## Slide 6
DeepGEMM Architecture
JIT compilation: first call compiles CUDA kernel, subsequent calls use cache
generate_normal → FP8 casting + TMA-aligned scale factors
transpose_fp32 helper: rearranges scale factors for TMA (padded stride 33 avoids bank conflicts)
fp8_gemm_nt → sm90_fp8_gemm_1d2d_impl kernel
generate_normal
→
transpose_fp32
→
sm90_fp8_gemm_1d2d_impl
6/36

## Slide 7
DeepGEMM — Perfetto Trace
CPU lane: fp8_deepgemm annotation → GPU lane: transpose_fp32 + sm90_fp8_gemm_1d2d_impl
Look for: ProfilerStep#2/3/4, kernel names, CPU-GPU gap
7/36

## Slide 8
DeepGEMM — Perfetto: bf16 Baseline
[SCREENSHOT: Perfetto bf16 trace]
CPU: bf16_matmul → aten::matmul → aten::mm
GPU: nvjet_tst_256x128_64x4_1x2_h_bz_coopA_NNT
3 ProfilerSteps × ~300µs each
8/36

## Slide 9
DeepGEMM — Perfetto: FP8 Trace
[SCREENSHOT: Perfetto FP8 trace]
CPU: fp8_deepgemm annotation
GPU: transpose_fp32 (8µs) + sm90_fp8_gemm_1d2d_impl (~195µs)
Note: transpose_fp32 has padded stride 33 to avoid SMEM bank conflicts
9/36

## Slide 10
Reading Kernel Names
bf16 cuBLAS
nvjet_tst_256x128_64x4_1x2_h_bz_coopA_NNT
nvjet = NVIDIA JetBLAS (Hopper cuBLAS)
tst = tensor-sparse-tensor variant
256x128 = CTA tile (rows × cols)
64x4 = 64 K-tile × 4 pipeline stages
1x2 = warp arrangement
h = Hopper architecture
bz = block-zero optimization
coopA = cooperative launch on A
NNT = layout (A=row, B=row, out=col)
FP8 DeepGEMM
sm90_fp8_gemm_1d2d_impl
sm90 = Hopper SM 9.0
fp8 = FP8 precision
gemm = General Matrix Multiply
1d = 1D scale on A (per-token)
2d = 2D scale on B (per-128×128 block)
impl = implementation kernel
10/36

## Slide 11
DeepGEMM — NCU Comparison
Metric | bf16 cuBLAS | DeepGEMM FP8
Duration | 375 µs | 251 µs
Compute Throughput | 91.6% | 67.1%
Memory Throughput | 70.7% | 54.5%
TMA Instructions | 344K | 59K
Memory BW | 969 GB/s | 543 GB/s
Wallclock (profiler) | ~600 µs | ~195 µs
bf16 is more efficient. FP8 is faster. Why? 2x Tensor Core FLOPS + half the data.
11/36

## Slide 12
NCU: bf16 GEMM — Speed of Light
[SCREENSHOT: NCU bf16 Speed of Light chart]
91.6% Compute Throughput — this is what ‘good’ looks like
NCU flags: “High Throughput — utilizing greater than 80%”
12/36

## Slide 13
NCU: DeepGEMM FP8 — Speed of Light
[SCREENSHOT: NCU FP8 Speed of Light chart]
67.1% Compute, 54.5% Memory — compute-bound with scale factor overhead
13/36

## Slide 14
NCU: Memory Data Path Comparison
bf16
TMA: 344K instructions
Data: 2.82 GB through pipeline
DSMEM: 382 instructions (uses SM clusters)
Memory BW: 969 GB/s
[SCREENSHOT: NCU bf16 memory diagram]
FP8 DeepGEMM
TMA: 59K instructions (6x fewer)
Data: 1.44 GB (half the data)
DSMEM: 0 (no cross-SM sharing)
Memory BW: 543 GB/s
[SCREENSHOT: NCU FP8 memory diagram]
14/36

## Slide 15
NCU: Occupancy — Both Kernels Are Resource-Heavy
Metric | bf16 | FP8
Registers/Thread | 168 | 168
Dynamic SMEM/Block | 213 KB | 216 KB
Theoretical Occupancy | 18.75% | 18.75%
Achieved Occupancy | 14.72% | 14.00%
Block Limit (Registers) | 1 | 1
Block Limit (Shared Mem) | 1 | 1
Grid Size | 132 (= 132 SMs) | 132
Cluster Size | 2 | 2
Both kernels use maximum on-chip resources. 1 block per SM. Low occupancy by design.
15/36

## Slide 16
DeepGEMM — NCU Key Findings
Barrier Stalls
4.3 cycles/warp (32.95% est. speedup)
Occupancy
14% achieved (18.75% theoretical) — limited by 168 regs + 216 KB SMEM
Shared Store Bank Conflicts
FP8: 12.55% vs bf16: 8.65% — FP8 pays extra for scale factor stores
"The scale factor overhead is the price of FP8 quantization"
16/36

## Slide 17
KERNEL 2
FlashAttention-3: Hopper-Native Attention
github.com/Dao-AILab/flash-attention (hopper/)
2.0–2.6x faster than FA-2 across all sequence lengths
17/36

## Slide 18
What Changed from FA-2 to FA-3
1
WGMMA
Warp Group MMA: larger Tensor Core tiles
2
TMA
Tensor Memory Accelerator: async bulk HBM → SMEM
3
Warp Specialization
Producer warps (TMA) overlap with consumer warps (WGMMA)
Plus: Ping-pong scheduling overlaps GEMM and softmax
18/36

## Slide 19
FA-3 vs FA-2 — Scaling Results
Seq Length | FA-2 (ms) | FA-3 (ms) | Speedup
512 | 0.059 | 0.031 | 1.89x
2048 | 0.980 | 0.474 | 2.07x
4096 | 3.698 | 1.667 | 2.22x
8192 | 14.054 | 6.593 | 2.13x
Consistent 2x across all sequence lengths — not a one-off optimization
19/36

## Slide 20
FA-3 — Kernel Names Tell the Story
FlashAttention-2
flash_fwd_kernel
Hand-written CUDA kernel, vendored in PyTorch
255 regs/thread (hardware max!)
0 TMA instructions — legacy ld.global only
211K local memory loads (register spills to HBM)
128 threads/block (4 warps)
FlashAttention-3
device_kernel
CUTLASS 3.x CuTeDSL template, Hopper-native
168 regs/thread (no spills!)
7.17K TMA instructions — hardware DMA engine
0 local memory loads (zero register spills)
384 threads/block (12 warps)
"From hand-tuned to template-generated — fewer registers, zero spills, hardware DMA"
20/36

## Slide 21
FA-3 — Perfetto Trace
[LIVE DEMO — Perfetto UI] FA-2 trace (flash_fwd_kernel) vs FA-3 trace (device_kernel) Same attention, different kernel, 2x faster
21/36

## Slide 22
FA-3 — NCU: The Register Spill Story
FA-2 (flash_fwd_kernel)
255 registers/thread — hardware maximum
211,970 local memory load instructions
Local memory = HBM round-trips!
L1TEX suggestion: 29.4% est. speedup
1/32 bytes utilized per sector (catastrophic)
FA-3 (device_kernel)
168 registers/thread — 87 fewer
0 local memory load instructions
7,170 TMA instructions (hardware DMA)
196.91 KB SMEM (vs 63.54 KB)
Data lives in SMEM, not registers
FA-3 uses FEWER registers but spills LESS
How? TMA offloads data movement from registers → hardware DMA engine. SMEM used aggressively (196 KB vs 63 KB) — data lives in shared memory, not registers.
22/36

## Slide 23
FA-3 — NCU: Speed of Light Comparison
[SCREENSHOT: NCU FA-2 Speed of Light]
[SCREENSHOT: NCU FA-3 Speed of Light]
FA-2: 28.6% compute, 30.4% memory
FA-3: 41.8% compute, 35.6% memory
Metric | FA-2 | FA-3
Duration (NCU) | 76.90 µs | 35.46 µs
Compute Throughput | 28.56% | 41.80%
Memory Throughput | 30.35% | 35.60%
Achieved Occupancy | 1.18% | 13.10%
23/36

## Slide 24
FA-3 — NCU: Memory Architecture
FA-2 Data Path
HBM → legacy ld.global → Registers → SMEM
49.96K global load instructions
0 TMA instructions
9.04% L1/TEX hit rate (cache thrashing)
63.54 KB dynamic SMEM per block
Register-heavy: 255/255 used
FA-3 Data Path
HBM → TMA → SMEM (bypasses registers!)
8.70K global load instructions (6x fewer)
7.17K TMA instructions
67.29% L1/TEX hit rate (7x better)
196.91 KB dynamic SMEM per block (3x more)
Register-light: 168/255 used
TMA bypasses registers entirely — hardware DMA loads 2D tiles from HBM to SMEM
24/36

## Slide 25
FA-3 — NCU Comparison (Verified on H200)
Metric | FA-2 (flash_fwd_kernel) | FA-3 (device_kernel)
Duration | 76.90 µs | 35.46 µs
Compute Throughput | 28.56% | 41.80%
Registers/Thread | 255 (max!) | 168
Block Size | 128 (4 warps) | 384 (12 warps)
Dynamic SMEM/Block | 63.54 KB | 196.91 KB
TMA Instructions | 0 | 7,170
Local Mem Loads | 211,970 (spills!) | 0
L1/TEX Hit Rate | 9.04% | 67.29%
Achieved Occupancy | 1.18% | 13.10%
Theor. Occupancy | 12.50% | 18.75%
FA-3: 2.17x faster, 11x better occupancy, zero register spills
25/36

## Slide 26
KERNEL 3
SonicMoE: IO-Aware MoE Kernels
github.com/Dao-AILab/sonic-moe (Tri Dao, Princeton / Together AI)
45% less activation memory, 1.86x faster than ScatterMoE
26/36

## Slide 27
Why MoE Kernels Are Hard
Each expert processes a variable number of tokens (varlen-M Grouped GEMM)
Fine-grained MoEs: small expert size → IO-bound, not compute-bound
Standard approach: gather tokens → pad → GEMM → scatter back
Gather
→
Pad
→
GEMM
→
Scatter
"The IO cost scales linearly with expert granularity"
27/36

## Slide 28
SonicMoE’s Key Innovations
1
Gather Fusion
Token gather fused with GEMM prologue (no separate kernel)
2
Ping-Pong Scheduling
Overlap epilogue IO with next tile’s MMA
3
Epilogue Fusion
SwiGLU + dS + A′ computed in GEMM epilogue
Result: IO is hidden behind compute
28/36

## Slide 29
SonicMoE — Profiler Results
Configuration: E=128, K=8, d=1536, n=256 (7B MoE)
35 TFLOPS on H200
Key Kernels:
quackgemm_actGemmGatedSm90 (up projection + SwiGLU fused)
quackgemm_default_epiGemmDefaultSm90 (down projection)
"Two GEMM kernels with fused activation — that’s the entire MoE forward"
29/36

## Slide 30
SonicMoE — Perfetto Trace
[LIVE DEMO — Perfetto UI] sonicmoe_forward annotation, two GEMM kernels, routing overhead
30/36

## Slide 31
SonicMoE — NCU Details
[SCREENSHOT: NCU SonicMoE kernel]
quackgemm kernel: occupancy, memory throughput, warp stall breakdown
31/36

## Slide 32
The Production Picture
DGX Spark profiling: DeepGEMM accounts for 61.9% of GPU time in DeepSeek-V4-Flash inference
SonicMoE beats DeepGEMM by 43% on forward pass for fine-grained MoEs (from their paper)
These GEMM kernels ARE the bottleneck in production
32/36

## Slide 33
Summary
Kernel | What | Speedup | Key NCU Insight
DeepGEMM FP8 | JIT FP8 GEMM | 3.09x vs bf16 | 67% compute, TMA-only data path
FlashAttention-3 | Hopper attention | 2.0–2.6x vs FA-2 | WGMMA + TMA + warp specialization
SonicMoE | IO-aware MoE | 35 TFLOPS | Gather fusion + ping-pong scheduling
33/36

## Slide 34
Takeaways
1
torch.profiler tells you WHAT happened
Open the trace in Perfetto
2
Nsight Compute tells you WHY
Roofline, occupancy, memory throughput
3
Kernel names are fingerprints
sm90, fp8, 1d2d, device_kernel, quackgemm
4
Profile first. Then optimize. Then profile again.
34/36

## Slide 35
Resources
▶ Workshop Repo
github.com/XAheli/torch-profiler
▶ DeepGEMM
github.com/deepseek-ai/DeepGEMM
▶ FlashAttention-3
github.com/Dao-AILab/flash-attention
▶ SonicMoE
github.com/Dao-AILab/sonic-moe
▶ Perfetto UI
ui.perfetto.dev
Aheli Poddar | Red Hat PyTorch Team
35/36

## Slide 36
How Fast Is Your Kernel, Really?
Thank You!
Aheli Poddar | Red Hat PyTorch Team
Questions?
36/36